## Slide 1
MEMS Microphone
Recorder System
PCB development, firmware bring-up, troubleshooting, and next deployment
Sam Amezcua | UC Davis | EDIT PRESENTATION DATE
0
1
2
3
4
5
6
7
FPC
ESP32-S3
WROOM
USB-C
FPC
SD
LiPo / power
PDM audio
local WAV
BLE control

## Slide 2
What I was building
A compact audio platform that works without a PC in the recording loop
Capture PDM MEMS microphone data as standard WAV files
Store recordings locally for untethered experiments
Trigger without touching the setup: pushbutton or Bluetooth
Make failures visible through LEDs, telemetry, and recoverable files
Support both a quick devkit prototype and custom microphone hardware
PLANNED USE — EDIT THIS LINE
[Replace with the exact final experiment/application.]
Current evidence supports describing it as a portable, remotely triggered acoustic-data platform for controlled or field measurements.
Design principle
Record first, verify continuously, and preserve usable audio when hardware or storage misbehaves.

## Slide 3
Three ordered PCB designs form the hardware path
Prototype quickly, scale the sensor geometry, then integrate the recorder
1 ESP32 devkit carrier
Rapid bring-up board
• ESP32-S3 DevKitC
• Two PDM microphones
• microSD + buttons + LEDs
• Platform used for firmware validation
2 Eight-mic flex array
Spatial sensor board
• Eight IMP34DT05TR PDM mics
• Four left/right microphone pairs
• Local decoupling
• 10-pin FPC tail
3 Integrated controller
Portable system direction
• ESP32-S3-WROOM-N8R8
• USB-C + LiPo charging
• 3.3 V and 1.8 V rails
• FPC, SD, buttons, and status LEDs
ESP32-S3
DevKitC
microSD
MIC L
MIC R
REC
0
1
2
3
4
5
6
7
FPC
ESP32-S3
WROOM
USB-C
FPC
SD
LiPo / power

## Slide 4
Board 1 — ESP32 devkit recorder
The fast-learning platform: prove the microphone, storage, controls, and enclosure before full integration
ESP32-S3
DevKitC
microSD
MIC L
MIC R
REC
48 kHz
stereo
16-bit PCM
microSD
What is on this board
• ESP32-S3 DevKitC module
• Two ST IMP34DT05TR PDM microphones
• 1.8 V microphone regulator
• microSD socket over SPI
• Record button and three status LEDs
• Exported STEP plus printable enclosure files
Validated pin map
PDM 4/5 • SD SPI 12/13/11/14 • button 35 • LEDs 40/41/42

## Slide 5
Board 2 — eight-microphone flex array
A narrow sensor strip for known microphone spacing and multi-point acoustic capture
0
1
2
3
4
5
6
7
FPC
MIC7
≈ 350 mm overall
MIC0 + FPC
Sensor layout
Eight ST IMP34DT05TR omnidirectional digital PDM microphones arranged along a narrow flex PCB.
Electrical strategy
Four left/right PDM pairs, shared clocking, paired data behavior, and local 100 nF / 10 µF decoupling.
System role
Moves the microphones away from the controller and enables repeatable spatial placement through one 10-pin FPC interface.
Design status: ordered PCB design; validate each pair, cable integrity, clock loading, and channel mapping during bring-up.

## Slide 6
Board 3 — integrated microphone controller
Turns the bench prototype into a battery-capable, connectorized recorder
ESP32-S3
WROOM
USB-C
FPC
SD
LiPo / power
USB-C + ESD
LiPo charge / load share
FPC sensor interface
Integration decisions
• ESP32-S3-WROOM-1-N8R8 replaces the plug-in dev board
• MCP73871 battery charging and load sharing
• Dedicated 3.3 V and 1.8 V regulation
• 10-position FPC connector for external mic hardware
• SD interface, USB access, controls, and visible status
• Mechanical mounting holes and compact enclosure path
Engineering shift
From “can this record?” to “can this be deployed, powered, connected, and recovered reliably?”

## Slide 7
Firmware evolved in five deliberate steps
Each intermediate build isolated one subsystem before combining them
1
PDM → serial
Captured raw PCM to a PC with a Python script.
2
USB microphone
Exposed the board as a USB Audio Class device.
3
SD diagnostic
Probed SPI behavior and swept mount speeds.
4
Standalone WAV
Recorded locally with button control and status LEDs.
5
BLE + reliability
Added remote control, telemetry, recovery, and storage guards.
Current recorder: bench validated and working

## Slide 8
The key reliability fix was separating capture from storage
SD writes are bursty; microphone sampling cannot wait
PDM microphones
48 kHz stereo
16-bit PCM
I²S + DMA
Hardware intake
deepened queue
Core 0 reader
Never touches
the SD card
128 KB pool
32 × 4 KB
≈680 ms headroom
Core 1 writer
WAV + periodic
flush/header update
Failure observed
A slow SD transaction could exceed the I²S DMA buffering. Samples were silently lost, so playback sounded sped up with clicks and pops.
Result after redesign
The reader runs continuously while storage latency consumes buffer headroom. Average SD throughput comfortably exceeds the 192 kB/s audio stream.
Control plane: button + BLE commands → start/stop | status path: LEDs + 500 ms BLE heartbeat

## Slide 9
Troubleshooting that materially changed the design
The project became robust by reproducing failures and adding explicit recovery paths
Observed problem
Root cause
Fix / lesson
Sped-up audio / clicks
SD writes blocked capture
Dedicated core-0 reader + 128 KB queue
SD failed after reset
Card left in partial SPI transaction
Send ≥74 clocks before every mount
Level LED froze with no card
Full mount retry ran every 50 ms
Separate 50 ms probe from 1 s remount
Pulled card ruined whole WAV
Header size updated only at stop
Refresh WAV header every 1 s
Old take overwritten
Flaky remount restarted filename scan
Monotonic in-RAM recording index
No serial / build too large
Board options were wrong
CDCOnBoot=cdc + huge_app partition
Upload port busy
IDE daemon held COM port
Stop the background Arduino CLI process

## Slide 10
What the recorder can do now
Bench-tested on the custom ESP32-S3 PCB
AUDIO
48 kHz • stereo • 16-bit PCM
Standard incrementing WAV files
CONTROL
Button or Bluetooth LE
Self-contained Web Bluetooth remote
PROOF
Live byte counter
Confirms data is actually reaching the card
STORAGE
20 MHz SPI on a 32 GB card
200 MB warning / 50 MB hard stop
RECOVERY
Hot-plug inference + periodic headers
At most ~1 s tail loss on card removal
STATUS
Three LEDs + 500 ms heartbeat
Recording, SD, free space, and error state
Known-good boot: SD mounted at 20 MHz → BLE advertising → ready to record

## Slide 11
Material damping check — feasibility only
A quick screen to learn what was possible and verify that the recorder produced analyzable data
What was done
Nine coverings × ambient / low / high hairdryer conditions. One short recording per combination; the source was hand-positioned.
Only takeaway
Bare pop-filter fabric looked promising (~12.5 dB lower recorded level than lid-off under high airflow). This is not calibrated attenuation or a scientific treatment comparison.
Presentation framing: engineering proof-of-concept and material down-selection—not a validated acoustic experiment.

## Slide 12
Next steps toward deployment
The core recorder works; the remaining work is board bring-up and application-specific validation
1
Define deployment
Replace the use-case placeholder with the exact study, placement, duration, and channel requirements.
2
Bring up ordered boards
Verify power rails → USB/flash → PDM clock/data → SD → BLE → multi-mic channel map.
3
Connect the flex array
Measure clock integrity, cable behavior, channel pairing, and simultaneous capture limits.
4
Package the system
Finalize mounting, enclosure, strain relief, acoustic opening, and environmental protection.
5
Run a controlled pilot
Use repeatable geometry, metadata, timing, and a validation recording before field deployment.
Main message
The project is now a working recording platform—not just a microphone breakout—and its reliability problems have defined the final hardware and firmware architecture.